## Slide 1: Kensington Volunteer Fire Department
2018 Pierce Arrow XT
Short Wheel Base Pumper
In Service March 11, 2018

## Slide 2: Purpose
This PowerPoint will briefly cover the differences between our 2014 and 2018 Pierce Arrow XT Short Wheel Base Pumpers.

## Slide 3: Stock Number 1-18-8630

## Slide 4: Fluids
2018 takes 10W30 CK-4 engine oil

## Slide 5: Cab Tilting
When tilting the cab, make sure the front bumper discharge is turned forward otherwise it will strike the cab.
Notes:
  Radiator hoses:
    2018 has rubber
    2014 has silicone
  Cab Tilt reservoir
    Do NOT fill when cab tilted. Will overflow when cab is lowered.

## Slide 6: Vehicle Specifications
Arrow XT custom chassis, Aluminum body
GVW – 48,500 lbs.
Length – 29’ 9.75”
Height – 9’ 5.5”
DDC DD13, 525 HP, EPA2016
Allison 4000, 6 speed, w/aggressive downshift program
Waterous CSU, 1,500 gallons per minute, Single Stage
Husky 3 foam system
Water – 750 gal.
Foam cell – 25 gal.
Fuel – 75 gal.
DEF – 4.5 gal.
Crew positions – 6
Governed speed – 68 mph.

## Slide 7: Insurance & Registration Card

## Slide 8: Fuel & DEF Doors
-4.5 gal. DEF tank
-75 gal. diesel tank w/fill on both sides

## Slide 9: Foam Controls Husky 3
Click to play a short video.

## Slide 10: Foam System Parts
Select Tank or Draft
Foam Drains
Valve must be in the vertical position to draft foam
Note: Make sure the cap is on prior
to moving lever off the “draft” position
otherwise you will have foam come out
on your feet.

## Slide 11: Foam Power Module

## Slide 12: Foam System Capacity Maximum Foam Solution Flow
0.01-3GPM
3% 100 GPM = 3 GPM of foam
1% 300 GPM = 3 GPM of foam
0.5% 600 GPM = 3 GPM of foam
0.3% 1000 GPM* = 3 GPM of foam
  *Maximum water flow will depend on plumbing restrictions*

## Slide 13: What lines are capable of flowing foam?
Front Bumper
  100’ of 1 ¾ hose with a 175 GPM @ 75 psi NP breakaway with a 15/16 tip
Crosslays
  200’ of 1 ¾ hose with a 175 GPM @ 75 psi NP breakaway with a 15/16 tip
LHR (400)
  400’ of 1 ¾ hose with a 175 GPM @ 75 psi NP breakaway with a 15/16 tip

## Slide 14: Maximum Foam Discharge Pump Pressure
This is VERY VERY VERY important:
The maximum Pump Discharge Pressure (PDP) when flowing foam is 150 psi.
This will affect the 400’ line off the rear.
*DO NOT EXCEED A PDP OF MORE THEN
150PSI WHEN FLOWING FOAM*

## Slide 15: Pump Panel

## Slide 16: Regeneration & Diesel Exhaust Fluid
Click to play a short video.

## Slide 17: Inventory

## Slide 18: Front Bumper
25’ of 5” with Stortz. One end has 5” Stortz to 4.5” NST for hydrant hook up.
100’ of 1 ¾” hose with 175 GPM @ 75 psi NP with 15/16” break a way nozzle. This line is foam capable.

## Slide 19: Driver Side Cab Compartment

## Slide 20: Drivers Side Compartment 1

## Slide 21: Drivers Side Compartment 1- Open
Drivers Gear Only!

## Slide 22: Drivers Side Compartment 2

## Slide 23: Drivers Side Compartment 2- Open
Hydra Ram with K Tool.

## Slide 24: Drivers Side Compartment 3

## Slide 25: Drivers Side Compartment 3- Open
30’ of 4” hose

## Slide 26: Rear
Left to Right:
-400’ of 1 ¾” with 175 GPM @ 75 psi NP with 15/16” tip (foam capable, however PDP must NOT exceed 150 psi when flowing foam)
-400’ of 3” with gated wye
-4” supply line
-4” supply line connected to the humat
-300’ of 2” of with 185 GPM @ 75 psi NP with 1 1/8 tip
-250’ of 2 ½ with 1 ¼ smooth bore

## Slide 27: Rear Compartment

## Slide 28: Rear Compartment Open
25’ of 5” with Stortz connections terminating to a 5” Stortz to 4.5” NST for hydrants
Remote Area Monitor Nozzle:
-500 GPM with fog tip

## Slide 29: Rear Camera
This is NOT to be used in place of a back up person!

## Slide 30: Rear Ladder Storage Compartment

## Slide 31: Rear Ladder Storage Compartment- Open
This box safely and securely holds the following:
-attic ladder
-elevator pole
-two hooks

## Slide 32: Air Intake

## Slide 33: Officers Side Cab Compartment

## Slide 34: Officers Side Cab Compartment- Open

## Slide 35: Officers Side Pump Panel
-50’ of 4” hose with Stortz to 4.5” NST for hydrants.
-Officers Halligan bar

## Slide 36: Officers Side Compartment 1

## Slide 37: Officers Side Compartment 1- Open
Two LED Vulcans
Metro Bag
Officers Bag (this MUST be taken with the standpipe racks)

## Slide 38: Officers Side Compartment 2

## Slide 39: Officers Side Compartment 2- Open
ALL EMS equipment must stay in this compartment. The only exception to this will be the ALS drugs.

## Slide 40: Questions?
Contact the following personnel:
  Deputy Fire Chief John “Red” Connell 301-641-1500
  FS05 (Captain Garcia and MFF Oliver)
  Chief Jayme Heflin