General – Turnout

____	Suede for holes and shrinkage – elbows, cuffs, knee pads

____	Discoloration on PBI surface If damaged the fabric will be week and tear when tested

____	Char or heat damage on PBI surface

____	Excessive grime and soot on PBI surface

____	Tar, paint and melted vinyl on PBI surface.

____	All PBI/Nomex for holes, rips, and/or abraded/worn areas – inside pockets as well Any hole requires repair

____	All seams for loose stitches – All layers - Any broken stitch requires repair

____	Velcro – No white – Should make the ripping sound when pulling apart

____	All reflective trim including lettering for damage or shrinkage

To test hold bright focused beam flashlight at eye level next to the temple 20 feet away from gear/trim. Compare brightness of new trim versus questionable trim.

Turnout Coat – Outer Shell

____ 	Collar for wear and holes

____ 	Throat tab stitching and Velcro

____ 	All double seams including pockets for broken stitches or loose threads

____	Both sleeves for holes and damaged scotchlite

____	Water wells for holes and delamination of Neoprene

____ 	Universal clip and radio pockets for loose stitches

____	Hook and Dee enclosure in front as well as all snaps

Pants – Outer Shell

____	Waist area for missing suspender buttons and holes where buttons should be

____	Hook and Dee closure at waist

____	Take-up straps on back waist with Velcro adjustments

Turnout Coat – Inner Liner

____ 	Velcro at neck line to insure hooking to outer shell

____	All snaps attaching to outer shell (sleeves, neck front and bottom hemline)

____	Hand/Wrist guards for wear and holes and delamination – pull wristlet apart to see holes

____	Quilted thermal liner for holes or burns

____	Binding around liner to be sure it is attached

Turnout Pants – Inner Liner

____	Quilted thermal liner for holes or burns

____	Gore-Tex® / CROSSTECH® moisture barrier for holes and delamination

____	Test all snaps that attach inner/outer shell at waist and at bottom of legs

Hoods

____	Any foreign substance on fabric

____	Char, heat damage, holes, melting on fabric surface

____	Loss of elasticity on face opening

____	Seam integrity

Gloves

____	Foreign substance (tar/paint) on fabric

____	Loss of elasticity/flexibility on finger movement

____	Loss of elasticity on gauntlet – pull gauntlet apart to inspect for holes

____	Seem integrity – check between fingers and thumb apex for 1st signs

____	Liner pullout

Helmets

____	Grime, soot, tar, or paint on shell

____	Fiberglass/Kevlar shell

- Cracks longer than 1 inch

- Any crack that is completely through the shell material

- Soft spots equal to or larger than the thumb pad

- Dull or chalky finish

- Bead trim secure to helmet and aluminum core not exposed

- Breakaway tabs (x2) present

____	Leather helmets

- Rib stitching cut or broken

- Exposed reinforcing wire

____	Face shield or Goggles

- Blistered, bubbled, cracked or charred

- Missing E-ring on face shield pivot

- Elasticity of goggle straps

____	PBI/Nomex earflaps for holes, rips, and/or abraded/worn areas

____	Earflaps for attachment to shell/liner

____	Suspensions

- Cracked, torn, or missing components

- Brittle and/or discolored straps

- Stripped adjustment/ratchet knob(s)

____	Reflective trim including lettering for charring, shrinkage, or missing

____	Chin Straps

- Missing, cut or broken stitching

- Strap torn or abraded

- Clogged or worn out Velcro

- Brittle or broken/missing quick release mechanism

Footwear

____	Foreign substance (tar/paint) on outer shell

____	Loss of elasticity/flexibility on flexation

____	Material damage – abrasion to toe/heel area, liner pull, pull tabs intact

____	Steel toe and shank damage – feel inside for deformity – check for toe depression

____	Sole tread wear