## Slide 1: Tractor Drawn Aerial
2016 Spartan ER
Chassis

## Slide 2
In addition to this presentation the following manuals should be read by all operators before operating the aerial.
Chassis Manual
Operators Manual
Tractor Drawn Aerial

## Slide 3: Table Of Contents
Specifications
Chassis
Jackknifing
Cab Controls
Vista Display
Transmission Fluid Check
Regeneration
Diesel Exhaust Fluid
Generator
Tiller Cab

## Slide 4: Specification Chart
GVWR 74,500 pounds
Front Axle 21,200 pounds
Rear Axle 29,000 pounds
Tiller Axle 24,300 pounds
Unit Height 11’ 3”
Unit Length 59’ 3”
Unit Width 9’ 11” mirror to mirror
Note – There are two vehicle placards in the Driver Compartment. The second placard has the most accurate axle weights after the Spartan Tiller axle modification.

## Slide 5: Specification Chart
Engine Cummins 500 HP
Brakes F-Disc R-Drum T-Disc
Tire Pressure F-115 R-125 T-130
Coolant Purple
Engine Oil 15W-40 48 Quarts
Transmission Fluid TES-295 39 Quarts
Power Steering Fluid Dexron III 8 Quarts
Diesel Exhaust Fluid 6 Gallons DEF

## Slide 6: Ladder Specifications
Vertical Operating Height 100 feet
Horizontal Reach 96 feet
Operating Range -10 to 75 degrees
Tip Load 500 pounds
Outrigger Spread 16 feet
Beam Extended
with Jacks Up 17 7 feet ½”
Ladder Pipe Rating 1000 gpm
Maximum wind speed 50 mph

## Slide 7: Chassis
Cab Locks
  All cab doors and compartments have electric locks
    Switches on Driver’s and Officers doors
Officer’s Door
Driver’s Door

## Slide 8: Chassis
Cab Locks
  Keypads located at driver and officer doors
  Key FOB also provided
  Stealth Switch

## Slide 9: Chassis
Glad Hands
  Located under driver side

## Slide 10: Chassis
Cameras
  The vehicle is equipped with 5 cameras to improve driver and tiller visibility
    Driver’s Mirror – facing rear
    Officer’s Mirror – facing rear
    Driver’s Rear Corner – facing front
    Officer’s Rear Corner – facing front
    Center Rear of Trailer – Back-up Camera

## Slide 11: Chassis
Cameras
Driver’s Mirror
Back-up Camera
Officer’s Mirror

## Slide 12: Chassis
Cameras
Driver’s Side Tiller Camera
Officer’s Side Tiller Camera

## Slide 13: Chassis
Cab Tilt
  Normal Operation
  Manual pump
  Direct 12v Override
  No Access Hatch

## Slide 14: Chassis
Cab Tilt
  Normal Operation
  Works same as Crimson Engine
  Battery switch on, ignition switch off
  Press up button until cab lock engages then stop
  DO NOT lower cab back onto lock

## Slide 15: Chassis
Cab Tilt
  In the event of 12v failure the cab can be manually raised
  Pump located rear of Officer Side Battery Box

## Slide 16: Chassis
Cab Tilt
  Direct 12v Override (SHOP USE ONLY)
  NOT a jumper stud

## Slide 17: Chassis
Cab Tilt
  There is no access hatch in the cab to check fluids
  Only tilt cab on weekly checks or when a defect requires it

## Slide 18: Chassis
Cab Tilt
  To lower cab pull cable attached to safety bar
  Press “D” button on cab tilt controller
  Continue to hold “D” button until light on controller turns off
  Light WILL NOT flash like Engines
Safety bar release cable

## Slide 19: Chassis
Battery Box
  Cover replacement important
  Climate control for batteries and DEF
  No sensors on covers

## Slide 20: Chassis
Engine Overview
  Officer’s Side

## Slide 21: Chassis
Engine Overview
  Driver’s Side

## Slide 22: Chassis
Generator PTO/Tiller Power Steering
  Always engaged
  Tiller Power Steering uses hydraulic fluid from the aerial system
  Fluid sight glass in compartment behind cab on officer’s side with cab tilt

## Slide 23: Chassis
Aerial PTO
  Switched on Dash

## Slide 24: Chassis
Parking Brake
  When protection valve is applied it applies the spring brake to the drive and tiller axles
  Service brake is applied to front steering axle
  Front Wheel Lock is eliminated

## Slide 25: Auxiliary Braking Device
This unit is equipped with an
Engine Brake AND Telma Retarder.
They will not be used in low traction or slippery conditions.

## Slide 26: Chassis
Locking Differential
  Drive axle has a true locking differential
  Makes both sides turn together
  Come to complete stop
  Activate on Vista Display
  Proceed at low speeds until traction is regained
  Come to a complete stop
  Disengage before continuing to drive

## Slide 27: Jackknifing
There are audible and visual jackknife indicators in both the cab and tiller cab
Tractor Jackknife Alarm

## Slide 28: Jackknifing
There are audible and visual jackknife indicators in both the cab and tiller cab
Trailer Jackknife Alarm

## Slide 29: Jackknifing
Two proximity sensors are located below the 5th wheel

## Slide 30: Jackknifing
The alarms are labeled “Approaching Jackknife”
The alarm begins to sound when you are approaching jackknife
The alarm continues to sound for the range of the sensor
The alarm STOPS when you have passed the sensor
Passing the sensor will cause damage to the vehicle

## Slide 31: Jackknifing
Jackknife alarm begins to activate

## Slide 32: Jackknifing
Jackknife alarm stops

## Slide 33: Jackknifing
Inside View
Outside View

## Slide 34: Jackknifing
Jackknife alarm begins to activate

## Slide 35: Jackknifing
Jackknife alarm stops

## Slide 36: Jackknifing
The unit MUST come to an IMMEDIATE STOP upon activation of the “Approaching Jackknife” alarm
The unit officer MUST disembark the unit and watch the inside pinch point until the unit has exited the jackknife

## Slide 37: Cab Controls

## Slide 38: Cab Controls
Display can toggle between:
  Vehicle
  Trip Odometer 1
  Trip Odometer 2
  Trip Odometer 3
  Settings
  EFLC Levels
  Diagnostics

## Slide 39: Cab Controls
Vehicle Screen will display:
  Transmission Oil Temp
  Engine Oil Temp
  Exhaust Temp
  Engine Coolant Temp
  Engine Oil PSI
  Turbo Boost PSI
  Primary Air Pressure
  Secondary Air Pressure
  Engine Load %
  Engine Torque %
  Battery Volts
  Fuel Level
  Vehicle Speed
  Engine Speed
  DEF Level
  Instant Fuel Economy
  Average Fuel Economy
  Engine Hours

## Slide 40: Cab Controls

## Slide 41: Cab Controls

## Slide 42: Cab Controls
All Electronic Switches
Seat Controls
  Driver seat is fully electrically adjusted

## Slide 43: Vista Display
Unit is equipped with multiplex wiring system
Display panel located on dash
Controls most major chassis electrical functions

## Slide 44: Vista Display

## Slide 45: Vista Display

## Slide 46: Vista Display

## Slide 47: Vista Display

## Slide 48: Vista Display

## Slide 49: Vista Display – Officer’s Side

## Slide 50: Vista Display – Officer’s Side
Officer CAN NOT control:
  Headlights
  Engine Brake
  Driveline Retarder
  Differential Lock
  Mud/Snow Setting
  Tire Chains

## Slide 51: Transmission Fluid Check
The Transmission Fluid level may be checked in the cab through the keypad selector.
The engine must be running at idle and the unit must be on level ground.
The engine must idle at least five minutes from a cold start.
The transmission must heat to at least 140 degrees F.
Push both the up and down arrows simultaneously on the keypad.
Arrows

## Slide 52: Transmission Fluid Check
After simultaneously pushing both buttons TRANS OIL will show on the screen
It will be followed by OK, -1 thru -7, or +1 thru +7. The – indicates under filled and the + indicates overfilled. The numeral indicates the number of quarts.
Any other message indicates a problem and CMF should be notified.
Always confirm the digital reading on the dipstick BEFORE adding fluid.
ONLY use Trans-Synd Fluid.

## Slide 53: Regeneration
All diesel exhaust systems must be fitted with a DPF and a regeneration system.
DPF is Diesel Particulate Filter which captures soot and ash from the engine exhaust.
Regeneration is the process of burning off the soot and ash.
There are two types of regeneration:
1. Passive which requires no driver involvement.
2. Active which requires driver involvement.
Warning lights in the dash cluster will advise the driver of what action is needed.

## Slide 54: Regeneration
Active Parked Regeneration
When the DPF lamp is solid a parked regeneration may be needed.
When the DPF lamp is flashing a parked regeneration is REQUIRED AS SOON AS POSSIBLE
During a regeneration exhaust temperature can reach 1300 degrees. Select an appropriate location.
Park unit, place the transmission in nuetral, engage parking brake, chock the wheel, and toggle the regeneration switch. Engine rpm should increase to approximately 1100rpm.
Keep exhaust 5 feet away from all objects and pedestrians.
The driver must remain with the vehicle during regeneration.

## Slide 55: Regeneration
Active Parked Regeneration
During the regeneration process the high exhaust temperature lamp will illuminate.
DO NOT complete regeneration in the Station or while connected to a Plymovent.
When the ECM determines the DPF has been regenerated engine rpm will decrease to normal rpm signaling the regeneration is over.
Remember exhaust components are still very hot.
If the regeneration process needs to be interrupted or stopped, depress the brake pedal.

## Slide 56: Regeneration
Active Parked Regeneration
Manual Regen Switch Location

## Slide 57: Regeneration
DPF/DEF Warning Lights

## Slide 58: Regeneration
Passive Regeneration
  Passive Regeneration will only occur when driving over 40mph
  It is unlikely that these trucks will drive enough highway miles for Passive Regeneration to complete it’s cycle

## Slide 59: Regeneration
Regeneration system will be disabled when the Aerial PTO is engaged

## Slide 61: Diesel Exhaust Fluid
Diesel Exhaust Fluid (DEF)
  Urea based fluid
  Designed to lower Nitrous Oxides in exhaust
  Follow recommended storage procedures for fluid in station.

## Slide 62: Diesel Exhaust Fluid
DEF Tank located in compartment inside left rear cab door
DEF Tank gauge located above fuel gauge on dash.

## Slide 63: Diesel Exhaust Fluid
Refill Procedures
  CMF stocks DEF in industry standard 2.5 Gallon Containers
  2 containers per case
  Each case comes with 2 filler tubes
  DEF is requested when ordering Station Supplies or as needed through FMRS.
  Any DEF container or filler tube that shows any signs of crystallization MUST be immediately discarded to avoid vehicle damage
  Any DEF spills or splashes should be diluted with water and cleaned

## Slide 64: Diesel Exhaust Fluid
Refill Procedures
  Only add DEF to the appropriate DEF tank
  DO NOT add DEF to the fuel tank
  DO NOT add fluid until the DEF level is at or below HALF (1/2)
  When DEF level reaches HALF, only add a single 2.5 gallon jug to the DEF tank using the supplied filler tube
  DO NOT top off DEF
  The empty jug AND filler tube MUST be thrown away. DO NOT RE-USE!!!

## Slide 65: 12 Volt Scene Lighting
All but 2 body mounted scene lights are 12 volt
Do not require generator power

## Slide 66: Generator
10kW PTO driven hydraulic generator
Generator located on trailer under aerial ladder
PTO always engaged
  Can be excited from Driver’s seat, Officer’s Seat, Tiller Cab, and Pedestal
  Powers tripod lights on back of cab, 120v outlets on body, cord reels, tiller HVAC

## Slide 67: Generator

## Slide 68: Generator
Generator control panel and circuit breaker panel located in small compartment above driver’s side outrigger

## Slide 69: Tiller Cab
“Push To Drive” Pedal
Camera Display
Switches
Axle Position Gauge
HVAC
Seat Controls

## Slide 70: Tiller Cab

## Slide 71: Tiller Cab
“Push To Drive” Pedal
  Must be pressed to place transmission in gear
  Must be done to come out of neutral EVERY time

## Slide 72: Tiller Cab
“Push To Drive” Pedal
  If the pedal is not pressed the driver will see the following indicators in the cab
“Range Inhibit” on dash
Flashing 6 on keypad

## Slide 73: Tiller Cab
Camera Display

## Slide 74: Tiller Cab

## Slide 75: Tiller Cab

## Slide 76: Tiller Cab
HVAC
  Both Air Conditioning AND Heat are run from the generator
  Uses a single residential style thermostat
  No diesel heater or fuel tank in the rear
  Generator can be turned on from tiller cab