## Slide 1
2021 Spartan/Rescue 1
Rescue Squad 717

## Slide 2: Key Differences vs. 2008 Pierce
Taller, Longer, Heavier
Manual generator transfer switch
Rated high anchor points
Stronger winches
Cab changing room

## Slide 3: Dimensions & Weight
Overall height: 10' 6"
Overall width:
  100" Body
  9' 8" Mirror to Mirror
Overall length: 39' 8”
Actual Weight – May 2022???
  Fully equipped with all tanks full and no personnel onboard
  Front axle – 23,000 lbs (GAWR)
  Rear axles – 54,000 lbs (GAWR)

## Slide 4: Safety Systems
Automatic Traction Control (ATC)
  applies the service brake to a spinning wheel so that the torque can be transferred through the differential to the wheel that has the traction
  reduces engine torque when both wheels are spinning to improve traction
  ATC light located in the cab will light when the ATC feature is active
  May be momentarily disengaged by “Offroad Traction” switch
Electronic Stability Control (ESC)
  stabilizes the vehicle during cornering maneuvers
  Compares where you are steering and where the vehicle is actually going
  Intervenes by applying the brakes to individual wheels asymmetrically in order to create torque about the vehicle's vertical axis
  system may reduce engine power or operate the transmission to slow the vehicle down

## Slide 5: Powertrain Systems
Motor: Cummins X12 500hp
Transmission: Allision 4000 EVS 5-speed
  TES-295 synthetic fluid
Maximum speed is 60 mph
Motor oil checked via front grille
Transmission level can be checked via the keypad

## Slide 6: Transmission Fluid
Fluid level check
  Selector in Neutral
  Temperature 140 to 220°F
  Engine at idle and parked for >2 minutes
  Level ground
Press both arrow buttons simultaneously to check fluid level; status displayed on selector pad screen
OL will be followed by OK, -1 thru -7, or +1 thru +7.
  The – indicates under filled and the + indicates overfilled.
  The numeral indicates the number of quarts.
Any other message indicates a problem and CMF should be notified.
Always confirm the digital reading by visually checking the dipstick BEFORE adding fluid.

## Slide 7: Cab Tilt
Confirm no overhead or front bumper obstructions
Turn ON cab master (battery) switch
Plug in controller
Press UP on controller until safety arm engages
Turn OFF master (battery) switch

## Slide 8: Cab Lowering
Turn ON cab master (battery) switch
Plug in controller
SLIGHTLY raise cab
While pulling release cable press and hold DOWN until red light goes out
Turn off Master (battery) switch

## Slide 9: Cab Tilt CAUTIONS
Always….verify clearances, secure loose items, and engage the safety arm
THIS CAB IS MUCH LONGER AND TALLER
Cab MUST be tilted outdoors
16 FEET
REQUIRED

## Slide 10: Data Plate

## Slide 11: Fluids
Motor oil – 45 quarts of 15W-40
Transmission fluid – 39 quarts of TES-295
Coolant – 54 quarts of Ext. Lift 50-50
Power Steering – 8 quarts of Dexron 3
Cab tilt – 6.8 quarts of Dexron 3
Fuel – 68 gallons of Diesel
Diesel Exhaust Fluid – 6 gallons of DEF
Generator oil – 10 quarts of 15w-40
Generator coolant – 14 quarts of Ethylene Glyco 50/50
Hydra-Qube (Winches) - 3-5 quarts of AW46 Hydraulic fluid

## Slide 12: Data Plate

## Slide 13: After-Engine Exhaust Treatment
Vehicle is equipped with diesel exhaust fluid and a diesel particulate filter
See Cummins After-Engine Treatment Brochure for more info.
DPF and exhaust temp warnings
Regeneration switches

## Slide 14: Regeneration Indicators

## Slide 15: Active Regeneration
Due to the type of travel typical of fire apparatus “active regeneration” is most common
Active regeneration occurs:
  When an intervention by the operator during travel or pumping operations creates correct conditions for regen
    Requires sufficient exhaust flow and temperatures
    Speedometer >5mph
    NO engine speed variations will occur when pumping or driving
  Manually by activating the DPF Regen switch while parked
Prevents system from entering or continuing in active regeneration mode; used when regen may engage in an undesirable location
Used to manually initiate a parked regeneration; DPF lamp must be illuminated to engage
Regeneration will not effect motor RPM during PTO operations if it engages automatically.

## Slide 16: Parked Regeneration
Do not perform regen inside a building or while attached to an exhaust removal system!
A minimum of 5 feet of clearance is required to the exhaust outlet.
When operating it may be necessary to inhibit regen if clearances to the exhaust are not available!

## Slide 17: Fuel & DEF
Diesel Fuel
  Fills on both sides of the apparatus at the rearmost wheel well
  68 gallon capacity
Diesel Exhaust Fluid (DEF)
  Fluid level displayed on dashboard gauge
  6 gallon tank
  Fill inside left rear cab door
  Must open access panel
  Light blue cap

## Slide 18: Exhaust System
Exhaust outlet is 6” diameter
  Pierce is 5”
PlymoVent boots will accept up to 6 ¼” exhaust outlets
  The fit is tight!
Check your mirror to ensure the hose disengages from the exhaust when exiting the station
Until the rubber molds to the larger tailpipe the boot may need to be manually disengaged
Slow and steady departures from the bay are necessary.

## Slide 19: Suspension & Brake Systems
23,000lb front axle
54,000lb rear axles
Parking brake
  2nd actuator located on officer's dash
Supplemental Brake for front axle
Anti-lock disc air brakes front and rear axle
26 cfm air compressor
12v auxiliary air compressor behind driver seat
  Powered by shoreline to maintain brake system while parked
Heated air dryer
Air tank drain actuators – driver side under D2 compartment
Officer side parking brake switch

## Slide 20: Suspension & Brake Systems
Front axle has traditional leaf springs
Rear axles have Neway AD-254 air suspension
  Axles independently suspended
  Dual height control valves ensure equal frame height regardless of loads

## Slide 21: Brakes – Front & Rear Axle
Meritor DiscPlus EX225 Disc
Pads must be replaced at 3mm (approximately 1/8”)
For additional information go to the Meritor Maintenance Manual
Wear indicator

## Slide 22: Brakes – Front Axle
Front axle has supplemental parking brake
Requires rear parking brake to be set first
Protection valve located in center of dash
HIGHLY Recommended for winching

## Slide 23: Jumper Studs & Glad Hands
Glad hands located under front of unit
Jumper studs located in driver door step well near shoreline

## Slide 24: Snow Chains
OnSpot automatic snow chains on drive axle
Locking switch located on dashboard above HVAC controls
The On-spot chains have a 5 second delay before they activate. This is done to prevent accidental activation.

## Slide 25: Shoreline
2 Independent 20-amp inlets
Lower yellow cover is for chassis shoreline
  Vehicle charging
  Power to two M18 chargers in the D2 and P2 compartments
Upper blue cover is for portable tool charging
These are not auto-eject plugs.
Must be unplugged manually before closing the cab door.

## Slide 26: Shoreline
20 amp, 120v NEMA 5-20 plug with Kussmaul display
Driver’s door must remain open when shoreline is connected
Supplies Kussmaul 35 amp battery conditioner and auxiliary air compressor
This is not an auto-eject plug.
Must be unplugged manually before closing the cab door.

## Slide 27: Keyless Entry
Holding down the ½ button will lock the cab doors.

## Slide 28: Portable Tool Power
Only provides power to power strips in crew compartment for equipment charging
Blue cover
This is not an auto-eject plug.
Must be unplugged manually before closing the cab door.

## Slide 29: Officer Seat Area
Cab Compartment Door Locks
Chassis alarm acknowledge
Parking brake control
Speedometer
Siren Brake

## Slide 30: Dashboard Display

## Slide 31: Driver’s Seat
Pnuematic
Lumbar
Support
Pnuematic release
Press to release lock to adjust seat forwards and backwards
Pnuematic
Lumbar
Support

## Slide 32: Warning Light Controls
Master switch located on center dash

## Slide 33: Cab/Compartment Door Locks
Electric door locks on cab entry doors
  Not connected to body compartments
Lock-out switch located behind front grill near oil fill
Key FOBs also provided
Lock-out button

## Slide 34: Starting & Stopping the Motor
Battery switch (MASTER), ignition switch, and start button are all grouped to left of steering wheel
Battery switch
Press to start the motor.
Engage for no more than 15 seconds.
Ignition switch
-ON for run
-OFF to shut off
In addition to the battery, ignition switch must be “on” for most electrical functions to work (like cab tilt)
Allow gauges to complete their sweep before attempting to start the motor. Failure to wait can result in false sensor alarms.

## Slide 35: Starting & Stopping the Motor
DO NOT leave the ignition switch in the ON position when the vehicle is not running.
Sequence of Master then Ignition is critical for Start-up

## Slide 36: Driver's Dash Controls

## Slide 37: Driver's Dash Controls
Seatbelt Indicator
Headlights
Up – Headlights
Middle – Marker Lights
Down - OFF
Engine Brake
Up – ON
Down - OFF
Engine Brake
Up – High
Middle - Medium
Down - OFF
Mud/Snow
Momentarily impairs ATC to allow more wheel spin; may be desirable in extra soft surfaces like snow, gravel, or mud
Chains
Pressing the switch up activates On-Spot Chains
Heated Mirror
Pressing the switch up turns on mirror heat

## Slide 38: Driver's Dash Controls
Auto Lube
Fault???
Horn Function
Up – Siren
Middle - Horn
Down – Air Horn
Wiper
Controls
Differential Lock
Locks drive axle side to side for improved traction
Interaxle Lock
Engages secondary rear axle for improved traction
HVAC Controls
Compartment
Locks
Dash
Dimmer

## Slide 39: VFD Information Display
Need info if there is any relevance about this

## Slide 40: Rear Camera
Located above the rear floodlight
Monitor flips down
Always active

## Slide 41: Reverse Floodlights
Floodlights activate when transmission placed in reverse
  Rear flood
  Rear-most flood on both sides

## Slide 42: SCBA Brackets – SmartDock
No straps or levers to restrain the SCBA or to release the SCBA - blue latching mechanism holds the SCBA in place during transit.
In the event of a collision, inertial forces cause the top latching mechanism to lock the SCBA in place, preventing it from becoming a projectile.
To release the SCBA, a smooth motion is required. Slow is smooth; smooth is fast.
With the SCBA straps donned, the wear should bend forward at the waist and stand up to release the tank from the upper claw.
If the tank is too loose or too tight within the claw there is an adjustment knob on top of the bracket.
For additional information view a quick video at https://www.youtube.com/watch?v=y43vJK3bsVo&app=desktop or check out the manufacturer’s website at https://www.imminet.com/products/fire-ems/smartdock/

## Slide 43: PTO Generator
35kW Onan
Located under walk-in behind D1 compartment
PTO located at 8 O'clock on transmission
Requires parking brake activation to engage
Engine speed under 900rpm to engage
Disengages over 1440rpm

## Slide 44: PTO Generator
Locking switch on center of dash to start
NOT to be used with vehicle in motion

## Slide 45: PTO Generator
Display above breaker panel in D1 compartment
FROG-D (Frequency Readout of Generator Display)
Displays Frequency, AMPS, and Volts
MODE button toggles to generator hours

## Slide 46: Diesel Generator
Stadco 18kW run, 22kW peak
Can only be started in P2 compartment
Generator located in center of body behind D2 and P2 body compartments
Access panel is located in D3 compartment

## Slide 47: Diesel Generator Start-up
Set Main load circuit breaker to "OFF"
Set Transfer Switch to position 2
Move toggle switch position to "ON"
Press "RUN"
Display can be used to check hours and load

## Slide 48: Diesel Generator
Has air plenum with 4-120v AC Fans
Fans draw air from intakes at top right rear of vehicle
Air cools generator
Bottom right breaker in panel MUST be on when generator is running

## Slide 49: Power Distribution
Breaker Panel in D1 Compartment
All breakers clearly labeled
Major items requiring AC power:
  Light Tower
  Air Compressor
  Plasma Cutter

## Slide 50: Cord Reels and Outlets
Hannay cord reels located in D2/O2 compartments
  200 feet of 10/4 wire
Outlets located on both sides of body
  Each side of front bumper
  Each side at rear wheel well
20 foot pigtail for plasma cutter
  250V / 100 Amp, 2-pole/3-wire watertight plug

## Slide 51: Scene Lighting
All body mounted scene lights are 12v LED
  Controlled in the cab
2 Brow Lights
3 Body Lights per side
1 Rear Light

## Slide 52: Light Tower
Will-Burt Night Scan PowerLite
  6 150W LED light heads
  Controller in D1 compartment
  Tower operates on chassis air and 12v DC power
  Lights operate on 120v AC power

## Slide 53: Light Tower
Controller Functions

## Slide 54: Light Tower – Start-up
Parking Brake MUST be engaged
Ensure no overhead obstructions
Ensure generator is on
Ensure E-Stop is not activated
Press Green Start button to power-up the mast

## Slide 55: Light Tower – Start-up
Raise Mast
  Double tapping "Mast Up" will take mast to 90 and turn on all lights
  Pressing and holding "Mast Up" will only operate while pressing the button (lights must be manually activated)
Raise mast to desired height
Tilt and Pan as desired

## Slide 56: Light Tower – Stowing
Double tap "Mast Down" button to Auto Stow
  Auto Stow is recommended
If not using Auto Stow press and hold "Mast Down" button until all LED's on controller turn off

## Slide 57: Manual Transfer Switch
Located on wall of the D1 compartment.
Transfer should be made under NO electrical load
Complete transfer before starting generators or turn off main breaker first

## Slide 58: Air Compressor
Jenny Air Compressor
  Rated to produce 27.2cfm at 175psi
  2 air storage tanks located in the Light Tower area.
    15 gallons each

## Slide 59: Air Compressor
Compressor located suspended in the P1 Compartment
  Fans integrated into compartment for cooling

## Slide 60: Air Compressor
Controls to start compressor in D2/O2 compartments

## Slide 61: Air Compressor
Tank drain located on front wall of O2 compartment

## Slide 62: Air Compressor
Weekly maintenance requirements marked on compressor

## Slide 63: Air Distribution
Controls in D2 compartment for
  Driver air reel (200' ½" hose, 120psi)
  Rear body connection

## Slide 64: Air Distribution
Controls in O2 compartment for:
  Officer air reel (200' ½" hose)
  Front bumper connection
NOTE difference between compressor and chassis connections

## Slide 65: Winches
Front and Rear winches are BOTH PTO driven
Same controller works both winches
Uses Harrison Hydra-Qube hydraulic system
PTO located at 8 O'clock on transmission
Only able to operate one at a time

## Slide 66: Winches – Hydra-Qube
All-in-one system
  Reservoir
  Heat Exchanger
  Filter
Mounted on roof near light tower
Contains 4.75 gallons of AW-46 hydraulic fluid

## Slide 67: Winches - Operation
Transmission MUST be in neutral
Parking brake MUST be applied
Turn on Winch PTO locking switch
Select desired winch
  Up for Front
  Down for Rear

## Slide 68: Front Winch
Ramsey H-600 Hydraulic Worm Gear Winch
Manual lever style clutch
12,000 pound pull rating
225 feet of 12 strand ½" Plasma Rope

## Slide 69: Rear Winch
Ramsey H-800 Hydraulic Worm Gear Winch
Air controlled clutch
25,000 max pull rating
135 Feet 12 strand 7/8" Plasma Rope

## Slide 70: Anchor Points
Crosby Swivel Tie Points (Upper Body)
  3 on each side of body
  2 on rear
  3500lb Working Load Limit
Rigging Receivers
  2 on each side of body
    1 centered between rear axles in body
    1 below body at rear corner
  12,000lb straight pull rating
Rear Rings (Tow Hooks)
  25,000 straight pull rating

## Slide 71: Additional Resources
This document and other supporting documents are available at
https://www.montgomerycountymd.gov/mcfrs-psta/driver/DriverTrainingPierceEnforcer.html
Members of the apparatus committee:
Assistant Chief Pete Friedman
Program Manager Steve Lamphier
Battalion Chief Monte Fitch
Captain Mike Green (Station 29)
Emergency Services Coordinator Ernie Krouse